Approximations in DFT 2/2
Claudio Attaccalite
CNRS/CINaM, Aix-Marseille Universite (FR)
Claudio Attaccalite
CNRS/CINaM, Aix-Marseille Universite (FR)
Claudio Attaccalite
CNRS/CINaM, Aix-Marseille Universite (FR)

---
From R. Gebauer’s slides

---
real-space grids

---
Quantum Espresso code
http://www.quantum-espresso.org/

---
Quantum Espresso code
Different executables for different tasks in QEDIR/bin
Documentation in QEDIR/Doc/INPUT_XX.txt
Code organization
pw.x	main code
pp.x	data analysis
ph.x	phonons/electron-phonon coupling
dos.x	density of states
bands.x plot band structure
pwcond.x transmitance
cp.x molecular dynamics
more tools avilable:
x-ray spectra, optics ,EELS, superconductivity,
magnetic resonance (NMR), Raman, etc..

---
Typical input file
 &control
    prefix='silicon',
    pseudo_dir='./'
    outdir = ‘./',
 /
 &system
    ibrav= 2,
    celldm(1) =10.2,
    nat= 2,
    ntyp= 1,
    ecutwfc = 12.0,
 /
 &electrons
 /
ATOMIC_SPECIES
 Si 28.086 Si.vbc.UPF
ATOMIC_POSITIONS {crystal}
 Si 0.00 0.00 0.00
 Si 0.25 0.25 0.25
K_POINTS automatic
2 2 2 0 0 0

---
Bravais Lattices: ibrav flag
https://en.wikipedia.org/wiki/Bravais_lattice
ibrav =1,3,2
ibrav =6, 7
ibrav =8, 9, 10, 11
ibrav =4, 5, -5
ibrav =12, -12, 13
ibrav =14

---
Typical input file
 &control
    prefix='silicon',
    pseudo_dir='./'
    outdir = ‘./',
 /
 &system
    ibrav= 2,
    celldm(1) =10.2,
    nat= 2,
    ntyp= 1,
    ecutwfc = 12.0,
 /
 &electrons
 /
ATOMIC_SPECIES
 Si 28.086 Si.vbc.UPF
ATOMIC_POSITIONS {crystal}
 Si 0.00 0.00 0.00
 Si 0.25 0.25 0.25
K_POINTS automatic
2 2 2 0 0 0

---
Typical input file
 &control
    prefix='silicon',
    pseudo_dir='./'
    outdir = ‘./',
 /
 &system
    ibrav= 2,
    celldm(1) =10.2,
    nat= 2,
    ntyp= 1,
    ecutwfc = 12.0,
 /
 &electrons
 /
ATOMIC_SPECIES
 Si 28.086 Si.vbc.UPF
ATOMIC_POSITIONS {crystal}
 Si 0.00 0.00 0.00
 Si 0.25 0.25 0.25
K_POINTS automatic
2 2 2 0 0 0

---
We will use only Norm-conserving pseudo
types: mt, vbc, hgh

---
Typical input file
 &control
    prefix='silicon',
    pseudo_dir='./'
    outdir = ‘./',
 /
 &system
    ibrav= 2,
    celldm(1) =10.2,
    nat= 2,
    ntyp= 1,
    ecutwfc = 12.0,
 /
 &electrons
 /
ATOMIC_SPECIES
 Si 28.086 Si.vbc.UPF
ATOMIC_POSITIONS {crystal}
 Si 0.00 0.00 0.00
 Si 0.25 0.25 0.25
K_POINTS automatic
2 2 2 0 0 0

---
Install QE on your PC
LINUX
LinuxMint or Ubuntu
use “synaptic” to install “quantum-espresso” and “xcrysden”
or type
sudo apt-get install quantum-espresso
sudo apt-get install xcrysden
MacOSX
Use MacPorts, open the terminal and type
sudo port install quantum-espresso
see here: https://ports.macports.org/port/quantum-espresso/
WINDOWS
download “putty” we will provide a server with QE and Octopus installed
https://www.putty.org/
Install the Quantum Mobile virtual machine
https://quantum-mobile.readthedocs.io/en/latest/
We will provide two laptops
with QE, Xcrysden and Octopus installed

---
First calculation:
Self-consistent calculation for Silicon in the diamond structure
Espace de Travail: /media/MateriApps
First tutorial: /media/MateriApps/tutorial/examples_pwscf_ex.tgz
Unpack files: tar zxvf tutorial/examples_pwscf_ex.tgz
Look the input file:
cd examples_pwscf_ex/
emacs si.scf.in
Run calculations!!
pw.x < si.scf.in > output_scf

---
Look the output file: check electrons, convergence, etc...

---
Using Xcrysden to verify input/output

---
Using Xcrysden to verify input/output

---
What can we do with the total energy?
Structure optimization, phonons, compressibility, phase transitions, binding energy, etc...

---
Second calculation:
Optimal lattice parameter for Silicon

---
Third calculation:
Silicon band structure
New calculation type
 &control
    calculation=’nscf’,
    prefix='silicon',
    pseudo_dir='./'
    outdir = ‘./',
 /
 &system
    ibrav= 2,
    celldm(1) =10.2,
    nat= 2,
    ntyp= 1,
    ecutwfc = 12.0,
    nbnd=8
 /
 &electrons
 /
ATOMIC_SPECIES
 Si 28.086 Si.vbc.UPF
ATOMIC_POSITIONS {crystal}
 Si 0.00 0.00 0.00
 Si 0.25 0.25 0.25
K_POINTS tbipa
Number of bands
k-points list in tbipa units
(k-points list in the k-point-path file)

---
Bands plot
 &bands
    prefix = 'silicon'
    outdir='./'
    filband = 'bands.dat'
 /
bands.in file
Run bands.x
bands.x < bands.in > output_scf
Plot with gnuplot
gnuplot
gnuplot> plot ‘bands.dat.gnu’ u 1:2 w l

---
4th calculation: data analysis
Charge density
Wave-functions
  &inputpp
    prefix = 'silicon'
    outdir='./'
    filplot = 'sicharge'
    plot_num= 7
    kpoint=1
    kband=4
    lsign=.true.
 /
 &plot
    iflag = 3
    output_format = 5
    fileout = 'si.bands4.xsf'
 /
  &inputpp
    prefix = 'silicon'
    outdir='./'
    filplot = 'sicharge'
    plot_num= 0
 /
 &plot
    iflag = 3
    output_format = 5
    fileout = 'si.rho.xsf'
 /
Run pp.x
pp.x < si.pp_rho.in > output_pp
Visualize with Xcrysden
xcrysden --xsf si.rho.xsf

---
Data Visualization with Xcrysden
Tools→ Data grid
Set Isolevel