Light induced real-time dynamics for electrons
“Quantum dissipation by swift nuclei
in condensed matter”
2022, Lausanne
Claudio Attaccalite
CNRS/CINaM, Aix-Marseille Universite (FR)

---
Light induced real-time
electron dynamics

---
Light induced real-time
electron dynamics

---
Light induced real-time
electron dynamics

---
Non-linear response
P(%omega) = P_0 + %chi^{(1)} E + %chi^{(2)} E^2 + O(E^3)
First experiments on linear-optics by P. Franken 1961
Ref: Nonlinear Optics and Spectroscopy
The Nobel Prize in Physics 1981
Nicolaas Bloembergen

---
We introduce an effective Hamiltonian that contains...
We start from the DFT
(Kohn-Sham) Hamiltonian:
1)
  universal, parameter free approach
{color green bold h_{bold k}}

---
We introduce an effective Hamiltonian that contains...
Renormalization of the band
structure due to correlation (GW)
2)
We start from the DFT
(Kohn-Sham) Hamiltonian:
1)
  universal, parameter free approach
{color green bold h_{bold k}}
{color green bold h_{bold k}} + {color blue {%DELTA bold h_{bold k}}}

---
We introduce an effective Hamiltonian that contains...
Renormalization of the band
structure due to correlation (GW)
2)
We start from the DFT
(Kohn-Sham) Hamiltonian:
1)
  universal, parameter free approach
{color green bold h_{bold k}}
{color green bold h_{bold k}} + {color blue {%DELTA bold h_{bold k}}}
3)
Charge fluctuations
(time-dependent Hartree)
{color green bold h_{bold k}} + {color blue {%DELTA bold h_{bold k}}} + {color magenta { bold V_{bold H} [ %DELTA %rho ]}}

---
We introduce an effective Hamiltonian that contains...
Renormalization of the band
structure due to correlation (GW)
2)
We start from the DFT
(Kohn-Sham) Hamiltonian:
1)
  universal, parameter free approach
{color green bold h_{bold k}}
{color green bold h_{bold k}} + {color blue {%DELTA bold h_{bold k}}}
4)
Electron-hole interaction
3)
Charge fluctuations
(time-dependent Hartree)
{color green bold h_{bold k}} + {color blue {%DELTA bold h_{bold k}}} + {color magenta { bold V_{bold H} [ %DELTA %rho ]}}
{color green bold h_{bold k}} + {color blue {%DELTA bold h_{bold k}}} + {color magenta { bold V_{bold H} [ %DELTA %rho ]}} + {color red {%SIGMA_{sex} [ %DELTA %igamma ] } }

---
Linear response
Wave-function in plane-waves plus norm-conserving pseudo
Propagation time about 50 fs, with a time-step 0.01 fs
Smearing included as non-Hermitian operator -ig (Weisskopf-Wigner)or in post-processing as in Octopus
Laser shape: delta function for LR/ sinus for Non-LR

---
Linear response
Wave-function in plane-waves plus norm-conserving pseudo
Propagation time about 50 fs, with a time-step 0.01 fs
Smearing included as non-Hermitian operator -ig (Weisskopf-Wigner)or in post-processing as in Octopus
Laser shape: delta function for LR/ sinus for Non-LR

---
The Gauge problem
bold H = { bold p^2 } over { 2 m } + bold r E +V( bold r)
Length gauge:
bold H = { 1 } over { 2 m } ( bold p - e A)^2 + V( bold r)
Velocity gauge:

---
The Gauge problem
bold H = { bold p^2 } over { 2 m } + bold r E +V( bold r)
Length gauge:
bold H = { 1 } over { 2 m } ( bold p - e A)^2 + V( bold r)
Velocity gauge:
Quantum Mechanics is gauge invariant,
both gauges must give the same results

---
The Gauge problem
bold H = { bold p^2 } over { 2 m } + bold r E +V( bold r)
Length gauge:
bold H = { 1 } over { 2 m } ( bold p - e A)^2 + V( bold r)
Velocity gauge:
Quantum Mechanics is gauge invariant,
both gauges must give the same results
… but in real calculations the each gauge choice
has its advantages and disadvantages

---
The Gauge problem
bold H = { bold p^2 } over { 2 m } + bold r E +V( bold r) + V_{nl} ( bold r, bold {r'})
In presence of a non-local
operator
these Hamiltonians
Are not equivalent anymore
{} neq { }
bold H = { 1 } over { 2 m } ( bold p - e A)^2 + V( bold r) + V_{ nl }( bold r, bold {r'} )
W. E. Lamb, et al. Phys. Rev. A 36, 2763 (1987)
M. D. Tokman, Phys. Rev. A 79, 053415 (2009)

---
The Gauge problem
bold H = { bold p^2 } over { 2 m } + bold r E +V( bold r) + V_{nl} ( bold r, bold {r'})
In presence of a non-local
operator
these Hamiltonians
Are not equivalent anymore
{} neq { }
bold H = { 1 } over { 2 m } ( bold p - e A)^2 + V( bold r) + V_{ nl }( bold r, bold {r'} )
moral of the story:
non-local potential should be introduce in length gauge and then transformed as
bold H = { 1 } over { 2 m } ( bold p - e A)^2 + V( bold r) + e^{ i A bold r} V_{ nl }( bold r, bold {r'} ) e ^{ -i A bold {r'} }
W. E. Lamb, et al. Phys. Rev. A 36, 2763 (1987)
M. D. Tokman, Phys. Rev. A 79, 053415 (2009)

---
The Gauge problem
Length gauge:
Non-local operators can be easily introduced
The dipole operator <r> is ill-defined in solids
you need a formulation in term of Berry-phase
bold H = { bold p^2 } over { 2 m } + bold r E +V( bold r)
Velocity gauge:
Non-local operators acquires a dependence
from the external field
The momentum operator <p> is well defined
also in solids
bold H = { 1 } over { 2 m } ( bold p - e A)^2 + V( bold r)
In recent years different wrong papers using velocity gauge
have been published (that I will not cite here)

---
In solids the polarization is written in terms of wave-function phase
P_%alpha = {2i e} over {(2 %pi)^3} int_{BZ} d bold k sum_{n=1}^{n_b} langle u_{n bold k} mline {partial } over { partial bold k_%alpha} mline u_{n bold k} rangle
King-Smith and Vanderbilt formula
Phys. Rev. B 47, 1651 (1993)
Berry's connection !!
it is a bulk quantity
time derivative gives the current
reproduces the polarizabilities at all orders
is not an Hermitian operator

---
Effective Schrodinger equation

---
Non-linear response of solids
Second Harmonic Generation
Design
P(%omega) = P_0 + %chi^{(1)} E + color red %chi^{(2)} E^2 + O(E^3)
Synthesis
Tetraphenyl Tetrel
Molecular Crystals
New molecular crystals with non-linear response comparable to LiNbO3 J. Phys. Chem. C, 126, 7, 3713–3726(2022)

---
Non-linear response of solids
Second Harmonic Generation
Design
P(%omega) = P_0 + %chi^{(1)} E + color red %chi^{(2)} E^2 + O(E^3)
Synthesis
Tetraphenyl Tetrel
Molecular Crystals
New molecular crystals with non-linear response comparable to LiNbO3 J. Phys. Chem. C, 126, 7, 3713–3726(2022)
Two-photon absorption
P(%omega) = P_0 + %chi^{(1)} E + %chi^{(2)} E^2 + color red %chi^{(3)} E^3
Phys. Rev. B 98, 165126(2019)

---
Intra-exciton spectroscopy (exp)
Phys. Rev. B 102, 201402(R) (2020)

---
Intra-exciton spectroscopy (exp)
C. Poellmann, et al .Nature Materials 14, 889 (2015)
S. Cha, et al. Nature Communications 7, 10768 (2016)
P. Steinleitner et al. Nano Letters 18, 1402 (2018)
P. Merkl,et al. Nature Materials 18, 691 (2019)

---
Intra-exciton spectroscopy (exp)
C. Poellmann, et al .Nature Materials 14, 889 (2015)
S. Cha, et al. Nature Communications 7, 10768 (2016)
P. Steinleitner et al. Nano Letters 18, 1402 (2018)
P. Merkl,et al. Nature Materials 18, 691 (2019)

---
Intra-exciton spectroscopy (exp)
MoS2
S. Cha, et al. Nature Communications 7, 10768 (2016)
[Speaker Notes: 250Khz 50 fs laser F = 24.4 MicroJaule cm- 2]

---
Pump and probe (theory real-time)
Induced polarization from the pump
%DELTA P( t ) = P_{ pp } ( t ) - P_{ p } ( t )
%DELTA P( %omega ) = int_{ t_{pp} }^{ infty } %DELTA P ( t ) e^{ i%omega t - %tau (t-t_{pp} ) }
%chi( %omega ) = {%DELTA P ( %omega ) }over { E_{probe}(%omega) }

---
Pump and probe (theory real-time)
Induced polarization from the pump
%DELTA P( t ) = P_{ pp } ( t ) - P_{ p } ( t )
%DELTA P( %omega ) = int_{ t_{pp} }^{ infty } %DELTA P ( t ) e^{ i%omega t - %tau (t-t_{pp} ) }
%chi( %omega ) = {%DELTA P ( %omega ) }over { E_{probe}(%omega) }

---
Pump and probe (theory real-time)
Induced polarization from the pump
%DELTA P( t ) = P_{ pp } ( t ) - P_{ p } ( t )
%DELTA P( %omega ) = int_{ t_{pp} }^{ infty } %DELTA P ( t ) e^{ i%omega t - %tau (t-t_{pp} ) }
%chi( %omega ) = {%DELTA P ( %omega ) }over { E_{probe}(%omega) }

---
Pump and probe (linear response)
We can get excited states from the solution
of the Bethe-Salpeter Equation (a Casida like equation)
left none mline %lambda right rangle = sum_{ c v bold k } A_{c v bold k } ^%lambda left none mline c v bold k right rangle
excited states are in the form:
Intra-exciton dipoles
%mu_{%lambda, %lambda'}^%alpha = langle %lambda' mline %mu^%alpha mline %lambda rangle = sum_{ c v bold k } sum_{ c' v' bold k' } A_{c v bold k }^{%lambda {}*{}} A_{c' v' bold k' }^ { %lambda'} langle c v bold k mline %mu^%alpha mline c' v' bold {k'} rangle
Linear response from an excited state
%chi^%lambda_{ %alpha,%beta } (%omega)= { 2 } over V N_%lambda sum_{ %lambda'} { { %mu_{%lambda' %lambda}^%alpha %mu^%beta_{ %lambda %lambda'} } over { E_%lambda' - E_%lambda - %omega + i%eta}}
+
-
=

---
Pump and probe (linear response)
Linear response vs real-time
%chi_%lambda^{ %alpha,%beta } (%omega)= { 2 } over V N_%lambda sum_{ %lambda'} { { %mu_{%lambda' %lambda}^%alpha %mu^%beta_{ %lambda %lambda'} } over { E_%lambda' - E_%lambda - %omega + i%eta}}
For m we used
velocity gauge
in order to avoid ill-defined and complicated
intra-bands dipole matrix elements
D. Sangalli, M. D’Alessandro, C. Attaccalite
https://arxiv.org/abs/2211.12241 (2022)

---
Pump and probe (group theory)

---
Pump and probe (group theory)
 E(2x)
Failure of hydrogen model for
localized excitons!!!

---
We need relaxation (for electron/excitons)

---
Exciton-phonon from first principle

---
Phonon-assisted absorption/emission

---
Exciton relaxation
C
C
Exciton-lifetime
M. Bernardi et al.
Phys. Rev. Lett. 125, 107401 (2020)
E. Malic
Nano Lett. 20, 4, 2849(2020)

---
C
Simple relaxation term in the Hamiltonian
Finite temperature absorption GaN
non-Hermitian term
tilde H = H + i %GAMMA
Derived from the
electron-phonon self-energy
%GAMMA_i prop Im %SIGMA^{ph}_{ ii } ( %omega = %epsilon_i )
tilde %epsilon_i (T)= %epsilon_i + i%eta( T)

---
Thank you for your attention
Non-linear response from real-time simulations including excitonic effect
Intra-exciton transition from first-principle
How to address relaxation in an efficient way?
Acknowledgments
Simone Sanna group
University Giessen
Davide Sangalli
CNR -Milan
Marco D’Alessandro
CNR - Rome
Pierre Lechifflart
Aix-Marseille Univ.

---
The Gauge problem
The guage transformation connect the different guages
A_2 = A_1 + nabla f
vector potential
%phi_2 = %phi_1 - 1 over c {partial f} over { partial t}
Arbitrary scalar
function
f( r,t)
scalar potential
%psi_2 = %psi_1 e^{-i e f(r,t)/hbar c}
wave-function phase
Non-local operators do not commute
with gauge transformation
V_{ nl }, %SIGMA_{ xc }, %DELTA^{GW}, etc.…

---
Design materials for non-linear optics
with ab-initio codes
Simone Sanna group
Justus Liebig University Giessen
Our prediction:
Tunable c2 in
LiNbxTa1-xO3
without affecting c3
Nonlinear optical response of ferroelectric oxides
Phys. Rev. Mat. 6 (6), 065202 (2022)
KNbO3 / LiNbO3 / LiTaO3
Properties
Design
Synthesis
Tetraphenyl Tetrel
Molecular Crystals
New molecular crystals with non-linear response comparable to LiNbO3 J. Phys. Chem. C, 126, 7, 3713–3726(2022)

---
Real-time Green’s functions
Kadanoff-Baym
equations
From Green’s functions to density matrix
Generalized Kadanoff-Baym Ansatz (GKBA)
Correspond to the equilibrium
self-energy

---
Electronic relaxation
2 – relaxation towards
quasi-equilibrium
3 – Measurement process
1 – Photo-excitation process
Sangalli, D., & Marini, A.
EPL (Europhysics Letters), 110(4), 47004.(2015)

---
Local-fields and excitonic effects
in h-BN monolayer
IPA
 independent particles
+quasi-particle corrections
+time-dependent Hartree (RPA)
+screend Hartree-Fock (excitonic effects)
[Speaker Notes: In fact, the IPA+GW shows two peaks: the first at about 4 eV is the shifted two-photon π → π∗ resonances peak which is attenuated by 40% with respect to IPA [Fig. 2 (a)]; the second very pronounced peak at about 8 eV comes from the interference of π → π ∗ one-photon resonances and σ → σ∗ two-photon resonances.]

---
Local-fields and excitonic effects
in h-BN monolayer
IPA
IPA + GW
 independent particles
+quasi-particle corrections
+time-dependent Hartree (RPA)
+screend Hartree-Fock (excitonic effects)
[Speaker Notes: In fact, the IPA+GW shows two peaks: the first at about 4 eV is the shifted two-photon π → π∗ resonances peak which is attenuated by 40% with respect to IPA [Fig. 2 (a)]; the second very pronounced peak at about 8 eV comes from the interference of π → π ∗ one-photon resonances and σ → σ∗ two-photon resonances.]

---
Local-fields and excitonic effects
in h-BN monolayer
IPA
IPA + GW
IPA + GW + TDSHF
 independent particles
+quasi-particle corrections
+time-dependent Hartree (RPA)
+screend Hartree-Fock (excitonic effects)
[Speaker Notes: In fact, the IPA+GW shows two peaks: the first at about 4 eV is the shifted two-photon π → π∗ resonances peak which is attenuated by 40% with respect to IPA [Fig. 2 (a)]; the second very pronounced peak at about 8 eV comes from the interference of π → π ∗ one-photon resonances and σ → σ∗ two-photon resonances.]

---
Alternatives to the Berry-phase
Unified formalism for calculating polarization, magnetization, and more in a periodic insulator
Kuang-Ting Chen and Patrick A. Lee
Phys. Rev. B 84, 205137(2011)
J. Phys. Chem. Lett. , 9, 24, 7045–7051 2018